## Slide 1: Outline
Dept. of ECE, Vemana IT
2
Introduction
Problem Statement
Objectives
Literature survey
Applications
Reference

## Slide 2: INTRODUCTION
This project aims to create an affordable, modular prosthetic arm that is specifically tailored to bridge the gaps of availability, affordability, and maintenance in India.
Using affordable materials and modular parts, the design will also enable simpler replacement and repair of parts without causing undue costs to users or leading to idle periods for them.
11 May 2025

## Slide 3: Problem Statement
11 May 2025
Current prosthetic arms are expensive, non-modular, hard to repair, and lack advanced mobility and sensor integration, limiting user comfort and functionality.
The project aims to develop affordable, modular prosthetic arm with cost-effective materials and integrated sensors for easy repairs, enhanced user experience, and improved mobility.

## Slide 4: Objectives
To develop a cost-effective, modular prosthetic arm for easy repairs and maintenance.
To integrate sensors to improve grip strength detection and joint movement control for better functionality.
To design a prototype of a prosthetic arm.
11 May 2025

## Slide 5: Literature review:
1. Beyond Humanoid Prosthetic Hands: Modular Terminal Devices That Improve User Performance
Focus should shift from human-like appearance to functionality
Task-specific, modular designs improve user performance
Users prioritize function, comfort, and ease of use over form
Simpler mechanisms often outperform complex hands
User-centered design leads to better acceptance and outcomes
Open-source, customizable prosthetics foster innovation
Performance should be measured by task success, not mimicry
11 May 2025
Notes: Received 24 August 2024; revised 1 December 2024 and 31 December 2024; accepted 8 January 2025. Date of publication 13 January 2025; Date of current version 23 January 2025.
1. Current prosthetic hands focus too much on mimicking human form
Most research prioritizes making prosthetic hands look and move like human hands.
This limits functionality for specific tasks, especially for people using them in industrial or manual work.
2. There's a mismatch between user needs and prosthesis design
Actual prosthesis users often care more about functionality, comfort, and ease of use than about appearance.
Many existing devices are underused or abandoned because they don't meet practical needs.
3. Modular, task-specific devices can outperform humanoid designs
Specialized terminal devices (e.g., hooks, pliers, tool adapters) allow better performance in specific activities.
Customization and modularity give users more control, adaptability, and efficiency.
4. User performance improves with simpler, more robust mechanisms
Simpler designs (fewer fingers, basic grip types) often provide better strength, reliability, and ease of maintenance.
Complex multi-fingered hands can be fragile and difficult to control.
5. Need for expanding beyond anthropomorphic benchmarks
Evaluation of prosthetic hands shouldn't only compare them to natural hands.
Should include benchmarks based on task-specific performance and user satisfaction for different environments (home, work, sports).
6. Importance of user-centered design approaches
Involving users early in the design process improves device acceptance and usability.
Understanding users’ daily tasks leads to more practical, empowering solutions.
7. Technological advances enable more modular prosthetics
3D printing, lightweight materials, and open-source hardware make it easier to develop interchangeable attachments and personalized components.
INTRODUCTION:
Millions globally suffer from upper limb difference (ULD), impacting their capabilities. Myoelectric prostheses offer a solution by utilizing electromyography to control artificial hands. However, despite advancements, multi-articulating myoelectric hands show minimal benefit over simpler prostheses, leading to user dissatisfaction due to limited functionality and dexterity. The anthropomorphic design, aiming to replicate human hands, is constrained by mechanical and control limitations. Functional, non-humanoid designs are rare but could offer advantages, especially with modularity for task-specific applications.
USES:
It introduces four open-source modular non-humanoid devices for flicking, screwdriving, picking/placing flat objects, and cutting paper. These devices replace fingers on the OLYMPIC hand, a modular prosthesis. The devices are designed to perform tasks that are difficult for conventional humanoid prosthetic hands. Each task requires complex coordination at the joint level of a humanoid hand in order to produce a relatively simple task-space output. The devices are designed to perform actions that have meaningful social and functional uses in many areas of daily life, but are difficult-to-impossible with conventional prostheses: flicking, screwdriving, picking and placing small flat objects, and using scissors.
ADVANTAGES:
Non-humanoid designs improve task performance, reduce user compensatory movement, and decrease task load compared to humanoid prostheses.
Case studies validate these benefits, emphasizing the importance of monitoring user task load for positive rehabilitation outcomes.
Humanoid prostheses were outperformed by non-humanoid devices in all tasks.
Non-humanoid terminal devices reduced compensatory motion, allowing participants to complete timed tasks and precision tasks with higher accuracy.
These reductions in mental, physical, and frustration demands.
DISADVANTAGES:
Functionality for individual tasks limited by device specificity.
Need for end effector change for daily functionality.
Desire for anthropomorphic appearance for social acceptance.
Key Points:
Problem: Myoelectric prosthetic hands have high rejection rates due to limited functionality and anthropomorphic design constraints.
Solution: Develop and evaluate modular, non-humanoid terminal devices tailored for specific tasks.
Devices: Four devices were created for flicking, screwdriving, picking/placing flat objects, and cutting paper, designed as replacements for fingers on the OLYMPIC hand.
Methodology: A control group study with participants without ULD compared non-humanoid devices against a humanoid prosthesis, measuring task performance, compensatory motion, and perceived task load. Case studies with two participants with ULD were also conducted.
Results: Non-humanoid devices significantly improved task performance, reduced compensatory movement, and decreased task load compared to the humanoid prosthesis.
Conclusion: Task-specific, non-humanoid terminal devices offer a promising approach to enhance prosthetic hand functionality and user satisfaction. They may also improve quality of life by facilitating social interactions.
Future Work: Further research is needed to optimize the mechanical implementation of these prostheses, explore haptic feedback, and investigate the psychological embodiment of non-humanoid prostheses.

## Slide 6: 2. Prosthetic Limb Attachment via Electromagnetic Attraction Through a Closed Skin Envelope
Electromagnetic attachment can replace traditional socket systems for improved comfort and function in prosthetics.
Biomechanical analysis and cadaveric dissections ensure implant size, shape, and surgical feasibility.
Power consumption of 33 W for suspension during walking is a key design consideration.
Thermal management is crucial, with skin temperature increasing by 15.4°C after 1000 steps.
Biocompatible implant materials (stainless steel, titanium- nitride) enhance comfort and reduce tissue damage.
Optimization of force and electromagnet mass is guided by a proposed cost function.
Future work will focus on reducing thermal issues for long-term use.
11 May 2025
Notes: Manuscript received 16 June 2023; revised 11 September 2023 and 14 November 2023; accepted 7 December 2023. Date of publication 13 December 2023; date of current version 23 April 2024
INTRODUCTION:
The pursuit of advanced robotic prosthetic limbs faces a significant challenge: the limitations of current socket-based attachment methods. These methods often lead to discomfort, tissue damage, and pain, resulting in patient dissatisfaction and high abandonment rates, disproportionately affecting underprivileged communities. Addressing the drawbacks of soft-tissue suspension, such as pistoning and skin irritation, and the risks associated with percutaneous osseointegration (OI), including infection, a novel socket suspension paradigm is introduced. This system utilizes electromagnetic attraction between a subcutaneous ferromagnetic implant in the residual bone and an electromagnet in the socket. This approach aims to transfer suspension loads directly from the prosthesis to the bone while maintaining a sealed skin envelope.
USES:
The electromagnetic attachment system is designed for prosthetic limbs and offers a potential solution to challenges associated with traditional socket-based attachments and percutaneous osseointegration. By employing a subcutaneous ferromagnetic implant and an external electromagnet, the system aims to improve comfort, reduce tissue damage, and minimize infection risks for individuals with amputation. This system has utility in transfemoral amputations and could be adapted for various amputation levels.
ADVANTAGES:
The primary advantage of this electromagnetic attachment system lies in its potential to mitigate the drawbacks of existing prosthetic attachment methods. Unlike socket-based systems, it transfers suspension loads directly to the bone, reducing pistoning and associated tissue breakdown. Compared to osseointegration, it maintains a sealed skin envelope, minimizing infection risk. Additional benefits include:
Improved Comfort: By reducing pressure on soft tissues.
Enhanced Limb Health: Prevents skin ulcers and irritation.
Customizable Attachment: Attractive force modulation via electromagnet control.
Reduced Healthcare Costs: By minimizing visits to prosthetists and complications.
Potential for wider applicability: Circumvents limitations of OI in dyscalculic amputations.
DISADVANTAGES:
Despite its potential advantages, the electromagnetic attachment system also presents certain disadvantages and challenges:
Power Requirements: Suspension during gait requires electrical power, necessitating a power source and potentially leading to heat generation.
Heating Concerns: Prolonged use may result in increased skin temperature, requiring thermal management strategies.
Electromagnet Mass: The added mass of the electromagnet in the socket could impact user comfort and mobility.
MRI Incompatibility: The ferromagnetic implant renders the system incompatible with magnetic resonance imaging (MRI).
Dependence on technology: Reliance on a functioning electromagnet for secure attachment.
OVERALL SUMMARY
The study offers a design framework for an electromagnetic prosthetic attachment system that employs an external electromagnet for direct skeletal connection and a bone-anchored ferromagnetic implant. Tested using electromagnetic simulations, cadaveric dissections, and biomechanical analysis, the device demonstrates the viability of supporting a prosthesis while walking with controllable power needs and little heating. The method enhances the functionality, comfort, and health of prosthetic limbs and presents a viable substitute for conventional socket-based and Osseo-integrated options.

## Slide 7: 3. Transcutaneous Magnet Localizer for a Self-Contained Myokinetic Prosthetic Hand
Traditional myoelectric prosthetic hands often rely on external sensors and surface electromyography (sEMG), which can be unreliable due to noise, inconsistent placement, and limited control fidelity. The challenge lies in developing an implantable, reliable, fully integrated system to accurately track muscle movements and convert them into intuitive prosthetic control without relying on external sensors or wires. The system is fully wearable, compact, and self-contained, with the magnetic sensors embedded in a cuff that comfortably fits around the forearm. It accurately detects magnet positions with about 3 mm precision, enabling fine control of the prosthetic hand.
11 May 2025

## Slide 8: 4. Neural Network-Based Lower Limb Prostheses Control Using Super Twisting Sliding Mode Control
Traditional robotic leg controllers, like PID controllers, often can't handle unexpected changes or disturbances, making walking less smooth and more difficult for users. This method that combines neural networks and a control technique called Super Twisting Sliding Mode Control. This approach allows the prosthetic leg to learn and adapt to different walking conditions in real time while staying stable and smooth. The goal is to make robotic legs move more naturally, safely, giving users better comfort and confidence while walking. The super twisting version control reduces the jerky “chattering” often found in such systems, resulting in smoother motion. This method enhances the comfort, stability, and functionality of making walking safer and more intuitive for amputees.
11 May 2025

## Slide 9: 5. A Low-Cost Lightweight Prosthetic Arm with Soft Gripping Fingers Controlled Using CNN
This project offers a low-weight, low-cost, and responsive prosthetic arm with EEG-based and vision-based control systems. The structure includes soft elastomer fingers pneumatically actuated and operated with CNN and SVM algorithms on EEG signals, with an achieved accuracy of 48% and a 17 ms inference time. Another model used camera-driven CNNs to perform gesture detection with an accuracy of 98.67% and effective soft gripping through Arduino-controlled servos. Although the prototype is superior in cost and rudimentary function, it does not possess complete articulation, sensory feedback, and dynamic testing in real-time. The long-term aim is to develop a safe, user-friendly prosthetic for people with nerve damage, particularly children.
11 May 2025

## Slide 10: 6. Finch: Prosthetic Arm With Three Opposing Fingers Controlled by a Muscle Bulge
The project is about prosthetic arms overcoming the shortcomings of conventional myoelectric and body-powered designs. Methodologies included the application of muscle bulge detection through photoelectric Sensors, gesture-controlled systems with MPU6050 accelerometers, Arduino Uno,RF modules, and 3D-printed structures with single linear actuators. Functional testing, such as SHAP, was conducted on amputees to test performance. Limitations as reduced gesture recognition, absence of sensory feedback, mechanical misalignment, and sensor noise. Future developments involve integration of flex sensors, Bluetooth connectivity, sophisticated AI-based gesture recognition, and feedback systems to improve usability, comfort, and functionality, eventually progressing toward increased dexterity and real-world applicability.
11 May 2025

## Slide 11
Vi-HaB is a wearable vibrotactile feedback system designed to restore proprioception in upper-limb prosthetic users.
It provides independent force feedback from every finger of a prosthetic or exoskeleton, utilizing vibrotactile actuators on an armband.
The slave side uses force-sensitive resistors (FSRs) mounted on a dummy hand to simulate touch and grasping events.
An Arduino Nano interprets the sensor signals and sends them to the vibrotactile motors placed around the upper arm.
Each motor is associated with a different finger, allowing spatial mapping of finger sensations independent of phantom limb sensations.
Tested with 14 subjects with upper-limb disability or phantom limb sensations. Achieved average accuracy of 82.04% across conditions.
Performance was either stable or slightly better under distraction, emphasizing Vi-HaB’s resilience in everyday conditions and proving to be reliable.
Vi-HaB is affordable, nonintrusive, and flexible, well-suited to rehabilitation, prosthetic training, VR, and teleoperation.
11 May 2025
7.Development and Testing of a Wearable Vibrotactile Haptic Feedback System for Proprioceptive Rehabilitation.

## Slide 12
ProACT is an immersive Augmented Reality (AR) platform that evaluates intelligent control strategies for prosthetic arms with high Degrees of Freedom (DoF).
It integrates Robot Operating System (ROS), Gazebo simulator, Unity engine, and Microsoft HoloLens 2 to provide a mixed-reality testbed.
Control is facilitated using an EMG armband and eye-tracking, enabling multiple interaction methods: direct joint, end-effector, gaze-assisted, and context-assisted control.
The prosthetic used is the Modular Prosthetic Limb (MPL) with 7-DoF in the arm and 20-DoF in the hand.
AR feedback and visual feedback increase user awareness and confidence, and compensatory body motion is monitored for analysis.
Two user studies were conducted using a modified Box-and-Blocks test with non-amputee participants to simulate manipulation tasks.
Study 1 compared all four control methods; Study 2 focused on direct vs. context-assisted control across extended trials.
Results showed higher success rates and user satisfaction with gaze- and context-assisted methods.
11 May 2025
8. ProACT: An Augmented Reality Testbed for Intelligent Prosthetic Arms

## Slide 13: APPLICATIONS
11 May 2025
Daily Life Assistance: Enabling users to perform everyday tasks such as eating, writing, and personal care, improving their quality of life.
Affordable Prosthetic Solutions: Providing an affordable, locally-made prosthetic arm, making it affordable for individuals in low-income or underserved areas.
Ease of Repair and Maintenance: The modular structure enables easy and rapid repair, reducing downtime and enhancing the user experience.
Disaster Relief and Emergency Assistance: Offering low-cost prosthetics to victims of accidents or natural disasters, enabling them to regain their independence.

## Slide 14: References
D. Chappell, B. Mulvey, S. Perera, F. Bello, P. Kormushev and N. Rojas, "Beyond Humanoid Prosthetic Hands: Modular Terminal Devices That Improve User Performance," in IEEE Transactions on Neural Systems and Rehabilitation Engineering, vol. 33, pp. 466-475, 2025, doi: 10.1109/TNSRE.2025.3528725.
W. Flanagan et al., "Prosthetic Limb Attachment via Electromagnetic Attraction Through a Closed Skin Envelope," in IEEE Transactions on Biomedical Engineering, vol. 71, no. 5, pp. 1552-1564, May 2024, doi: 10.1109/TBME.2023.3342652.
V. Ianniciello, M. Gherardini and C. Cipriani, "Transcutaneous Magnet Localizer for a Self-Contained Myokinetic Prosthetic Hand," in IEEE Transactions on Biomedical Engineering, vol. 71, no. 3, pp. 1068- 1075, March 2024, doi: 10.1109/TBME.2023.3325910.
11 May 2025

## Slide 15: References
A. T. Demora and C. M. Abdissa, "Neural Network-Based Lower Limb Prostheses Control Using Super Twisting Sliding Mode Control," in IEEE Access, vol. 13, pp. 24929-24953, 2025, doi: 10.1109/ACCESS.2025.3538689.
A. Sahbel, M. Elaydi, A. Nasif, N. Sobhy, A. Magdy, and A. Abbas, “A Low-Cost Lightweight Prosthetic Arm with Soft Gripping Fingers Controlled Using CNN,” in 2024 14th International Conference on Electrical Engineering (ICEENG), 145-147, 2024, doi: 10.1109/ICEENG58856.2024.105664.
M. Yoshikawa, K. Ogawa, S. Yamanaka, and N. Kawashima, “Finch: Prosthetic Arm With Three Opposing Fingers Controlled by a Muscle Bulge,” in IEEE Transactions on Neural Systems and Rehabilitation Engineering,vol.31,377/386,2023,doi:10.1109/TNSRE.2022.3223531.
11 May 2025

## Slide 16: References
R. Yunus et al., "Development and Testing of a Wearable Vibrotactile Haptic Feedback System for Proprioceptive Rehabilitation," in IEEE Access, vol. 8, pp. 35172-35184, 2020, doi: 10.1109/ACCESS.2020.2975149.
S. Guptasarma and M. D. Kennedy, "ProACT: An Augmented Reality Testbed for Intelligent Prosthetic Arms," in IEEE Transactions on Neural Systems and Rehabilitation Engineering, vol. 33, pp. 354-365, 2025, doi: 10.1109/TNSRE.2024.3521923.
Alvarado, J. A. C., & Balderas, M. F. B. "Transradial Prosthesis: Development of a Bionic Arm Using an EEG Sensor.“ 2023 International Conference on Electronics, Communications and Computers(CONIELECOMP),1.6,2023.doi:10.1109/CONIELECOMP 57887.2023.10582117.
11 May 2025